## Slide 1
Offer Grembek
Co-Director, UC Berkeley, SafeTREC
Road Safety Management for Pedestrians and Bicyclists
Presented at
School of Transportation Engineering, Tongji University
October 26, 2015

## Slide 2: Research Collaborators
UC Berkeley
Offer Grembek, PhD
David Ragland, PhD, MPH
Julia Griswold, PhD
Aditya Medury, PhD
Yuanyuan Zhang, PhD
Frank Proulx
Jessica Nguyen
Semich Chousein
University of Minnesota
Robert Schneider, PhD
Tongji University
Junhua Wang, PhD
Ying Ni, PhD

## Slide 3: The Traffic Safety Problem in CA
Over 34,000 traffic fatalities in the past 10 years.
Facts and Figures
33%↓
* Source: Fatality Analysis Reporting System (FARS), NHTSA
2013 Figures
3,000 fatalities
* Source: Fatality Analysis Reporting System (FARS), NHTSA

## Slide 4: The Traffic Safety Problem in CA
Over 34,000 traffic fatalities in the past 10 years.
Since 2010 (end of recession) there is a 10% increase in fatalities
Facts and Figures
33%↓
* Source: Fatality Analysis Reporting System (FARS), NHTSA
2013 Figures
3,000 fatalities
* Source: Fatality Analysis Reporting System (FARS), NHTSA
10%↑

## Slide 5: Passenger Vehicle Fatalities
Facts and Figures
2013 Figures
1,611 fatalities
* Source: Fatality Analysis Reporting System (FARS), NHTSA
Over 21,000 passenger vehicle fatalities in the past 10 years.
10%↑

## Slide 6: Passenger Vehicle Fatalities
Facts and Figures
2013 Figures
1,611 fatalities
* Source: Fatality Analysis Reporting System (FARS), NHTSA
Over 21,000 passenger vehicle fatalities in the past 10 years.
Since 2010 (end of recession) there is a 1% increase in passenger vehicle fatalities
10%↑
1%↑

## Slide 7: Pedestrian Fatalities Increased
Facts and Figures
2013 Figures
701 fatalities
* Source: Fatality Analysis Reporting System (FARS), NHTSA
Over 6,500 pedestrian fatalities in the past 10 years.
10%↑
1%↑

## Slide 8: Pedestrian Fatalities Increased
Facts and Figures
2013 Figures
701 fatalities
17%↑
* Source: Fatality Analysis Reporting System (FARS), NHTSA
Over 6,500 pedestrian fatalities in the past 10 years.
Since 2010 (end of recession) there is a 17% increase in pedestrian fatalities
10%↑
1%↑

## Slide 9: Bicycle Fatalities Increased
Facts and Figures
2013 Figures
141 fatalities
Over 1,100 pedestrian fatalities in the past 10 years.
* Source: Fatality Analysis Reporting System (FARS), NHTSA
17%↑
10%↑
1%↑

## Slide 10: Bicycle Fatalities Increased
Facts and Figures
2013 Figures
141 fatalities
Over 1,100 pedestrian fatalities in the past 10 years.
Since 2010 (end of recession) there is a 41% increase in bicycle fatalities
41%↑
* Source: Fatality Analysis Reporting System (FARS), NHTSA
17%↑
10%↑
1%↑

## Slide 11: P/B Fatalities are Increasing
* Source: Fatality Analysis Reporting System (FARS), NHTSA
41%↑
17%↑
10%↑
1%↑
While passenger vehicles fatalities remained the same,
pedestrian and bicycle fatalities have increased significantly over the past four years.

## Slide 12: Relative Vulnerability in Traffic

## Slide 13: The Vulnerability Matrix
* SWITRS 2005-2009, Injury crashes of two parties or less.
Table from Grembek (2010)

## Slide 14: The Vulnerability Matrix
* SWITRS 2005-2009, Injury crashes of two parties or less.
Table from Grembek (2010)

## Slide 15: The Vulnerability Matrix
* SWITRS 2005-2009, Injury crashes of two parties or less.
Table from Grembek (2010)

## Slide 16: The Vulnerability Matrix
* SWITRS 2005-2009, Injury crashes of two parties or less.
Table from Grembek (2010)

## Slide 17: The Vulnerability Matrix
* SWITRS 2005-2009, Injury crashes of two parties or less.
Table from Grembek (2010)

## Slide 18: The Vulnerability Matrix
* SWITRS 2005-2009, Injury crashes of two parties or less.
Table from Grembek (2010)

## Slide 19: The Vulnerability of Pedestrians
40,202
1,088
= 36.95 – Relative vulnerability of pedestrians in the CA network
In other words: pedestrians suffer 36.95 times more injuries than they inflict.
* SWITRS 2005-2009, Injury crashes of two parties or less.
Table from Grembek (2010)

## Slide 20: The Vulnerability of Bicyclists
37,821
2,542
= 14.88 – Relative vulnerability of bicyclists in the CA network
In other words: pedestrians suffer 14.88 times more injuries than they inflict.
* SWITRS 2005-2009, Injury crashes of two parties or less.
Table from Grembek (2010)

## Slide 21: P/B are the Most Vulnerable
Tables from Grembek (2010)

## Slide 22: Safety is Obtained by Buffers
Environment
Industry
Road User
Passenger Vehicles

## Slide 23: Safety is Obtained by Buffers
Environment
Industry
Road User
Passenger Vehicles
Environment
Industry
Road User
Pedestrians and Bikes

## Slide 24: Limited P/B Industry Safety Buffer
Environment
Industry
Road User
Passenger Vehicles
Environment
Industry
Road User
Pedestrians and Bikes

## Slide 25: Principles of Road Safety Management
 | 1 | 2
3 | 4 | 5
6 | 7 | 8
A set of goals and activities to improve P/B safety | Infrastructure data | Exposure data
Data Evaluation | Hazard Assessment | Countermeasure Selection
Economic Appraisal | Funding Sources | Institutionalization

## Slide 26: Principles of Road Safety Management
 | 1 | 2
3 | 4 | 5
6 | 7 | 8
A set of goals and activities to improve P/B safety | Infrastructure data | Exposure data
Data Evaluation | Hazard Assessment | Countermeasure Selection
Economic Appraisal | Funding Sources | Institutionalization

## Slide 27: Principles of Road Safety Management
 | 1 | 2
3 | 4 | 5
6 | 7 | 8
A set of goals and activities to improve P/B safety | Infrastructure data | Exposure data
Data Evaluation | Hazard Assessment | Countermeasure Selection
Economic Appraisal | Funding Sources | Institutionalization

## Slide 28: Principles of Road Safety Management
 | 1 | 2
3 | 4 | 5
6 | 7 | 8
A set of goals and activities to improve P/B safety | Infrastructure data | Exposure data
Data Evaluation | Hazard Assessment | Countermeasure Selection
Economic Appraisal | Funding Sources | Institutionalization

## Slide 29: Principles of Road Safety Management
 | 1 | 2
3 | 4 | 5
6 | 7 | 8
A set of goals and activities to improve P/B safety | Infrastructure data | Exposure data
Data Evaluation | Hazard Assessment | Countermeasure Selection
Economic Appraisal | Funding Sources | Institutionalization

## Slide 30: Principles of Road Safety Management
 | 1 | 2
3 | 4 | 5
6 | 7 | 8
A set of goals and activities to improve P/B safety | Infrastructure data | Exposure data
Data Evaluation | Hazard Assessment | Countermeasure Selection
Economic Appraisal | Funding Sources | Institutionalization

## Slide 31: Principles of Road Safety Management
 | 1 | 2
3 | 4 | 5
6 | 7 | 8
A set of goals and activities to improve P/B safety | Infrastructure data | Exposure data
Data Evaluation | Hazard Assessment | Countermeasure Selection
Economic Appraisal | Funding Sources | Institutionalization

## Slide 32: Principles of Road Safety Management
 | 1 | 2
3 | 4 | 5
3 | 7 | 8
A set of goals and activities to improve P/B safety | Infrastructure data | Exposure data
Data Evaluation | Hazard Assessment | Countermeasure Selection
Economic Appraisal | Funding Sources | Institutionalization

## Slide 33: Principles of Road Safety Management
 | 1 | 2
3 | 4 | 5
3 | 7 | 8
A set of goals and activities to improve P/B safety | Infrastructure data | Exposure data
Data Evaluation | Hazard Assessment | Countermeasure Selection
Economic Appraisal | Funding Sources | Institutionalization

## Slide 34: Principles of Road Safety Management
 | 1 | 2
3 | 4 | 5
6 | 7 | 8
A set of goals and activities to improve P/B safety | Infrastructure data | Exposure data
Data Evaluation | Hazard Assessment | Countermeasure Selection
Economic Appraisal | Funding Sources | Institutionalization

## Slide 35: Principles of Road Safety Management
 | 1 | 2
3 | 4 | 5
6 | 7 | 8
A set of goals and activities to improve P/B safety | Infrastructure data | Exposure data
Data Evaluation | Hazard Assessment | Countermeasure Selection
Economic Appraisal | Funding Sources | Institutionalization

## Slide 36: Facility decomposition

## Slide 37: Elements and core facilities
Sidewalk
Buffer
Approach
Median
Approach
Buffer
Sidewalk
Crosswalk
Intersection

## Slide 38: Define an approach
N1
N2
A1
A2

## Slide 39: Formal Infrastructure Database
Notes: If we realize this structure into the database, we can see there are two core tables recording each node and approach, in the red box. And all the other sub-tables will link to the two red tables through the foreign key. For example, the foreign key in a buffer is the approach ID for that buffer. And you can find the approach ID in the approach table.

## Slide 40: Labeling nodes and approaches
Notes: The nodes includes intersections, segment breaks, underpass/overpass; approaches are segments connect nodes in different travel directions. They are the basic components in the database, onto which other elements are connected. Create a new map in google maps. Name the map, add points at the location of the nodes, new lines along the segments. Then name them in 7 digits, first 3 for route name and left 4 digits for squence.

## Slide 41: Computer data collection
Notes: To conduct the work more efficienctly, we use double screen. One is to navigate in the map, the other is to input the data.

## Slide 42: Principles of Road Safety Management
 | 1 | 2
3 | 4 | 5
6 | 7 | 8
A set of goals and activities to improve P/B safety | Infrastructure data | Exposure data
Data Evaluation | Hazard Assessment | Countermeasure Selection
Economic Appraisal | Funding Sources | Institutionalization

## Slide 43: Pedestrian Crashes
Absolute Number of Crashes

## Slide 44: Pedestrian Crashes
Absolute Number of Crashes

## Slide 45: Pedestrian Crash Risk
Crash Risk:
(Crashes / Exposure)

## Slide 46: Pedestrian Crash Risk
Crash Risk:
(Crashes / Counts)

## Slide 47: Why model pedestrian exposure?
1000s of intersections in the SHS
Data collection at all intersections is impractical
Model can provide estimates for locations without counts

## Slide 48: Pedestrian exposure can be modelled using regression
Pedestrian Exposure =
f(Environmental Characteristics)

## Slide 49
Dependent Variable: pedestrian crossing counts
Explanatory Variables:
  Land Use: population, households, school, businesses
  Transportation: street network, design, infrastructure
  Other: vehicle ownership, slope

## Slide 50: Site-level explanatory variables
Number of Lanes
Traffic signal
AADT

## Slide 51: Buffer-level explanatory variables
0.5 mi.

## Slide 52: Buffer-level explanatory variables
Street Connectivity = Number of street segments

## Slide 53: Buffer-level explanatory variables
Land Use -Number of households

## Slide 54: Pilot model based on 60 observations
Estimated annual crossings at urban arterials =
exp (0.00364 × number of households within 0.1 miles
+ -7.17×10-5 × total AADT
+ 8.96×10-10 × total AADT2
+ 0.367 × number of lanes on cross street
+ 12.5)
Adjusted R-square = 0.85

## Slide 55: Full model is being developed
429 studies
5,200+ hours of counts
270+ unique locations

## Slide 56: Calculate Pedestrian Crash Risk
Estimate risk at locations without counts

## Slide 57: Principles of Road Safety Management
 | 1 | 2
3 | 4 | 5
6 | 7 | 8
A set of goals and activities to improve P/B safety | Infrastructure data | Exposure data
Data Evaluation | Hazard Assessment | Countermeasure Selection
Economic Appraisal | Funding Sources | Institutionalization

## Slide 58: Hazard Assessment
Spot Approach
Hotspots or High Collision Concentration Locations (HCCL) are road segments with a higher than expected number of crashes, compared to prior experience or a user-defined threshold.
Systemic Approach
Systemic approach identifies a set of locations where countermeasures may be installed systemically where roadway facilities share the same unsafe features that are associated with particular crash types.

## Slide 59: Systemic Approach vs. Spot Approach
Benefits
Complement the hotspot approach
Reduced data needs
Widespread effect
Crash type prevention
Cost‐effectiveness
Drawbacks
Justifying blanket improvements can be difficult

## Slide 60: Elements of HCCL Identification
Filtering relevant collisions
Algorithms to identify HCCLs
Generating a list of HCCLs
Input: Collision Data
TSAR Files
Location types, party types, years, etc.
Selection criteria:
maximum window length, minimum number of collisions
Starting and ending postmiles, total number of collisions, other supplementary information
Pedestrian Safety Monitoring Report (PSMR) Tool

## Slide 61
1
2
3
5
4
6
0
0.2
0.4
0.6
0.8
1.0
7
9
8
Postmile
Illustrative Example
Road network
Individual Crash Locations
Maximum window length (w): 0.1 miles
Minimum crash threshold (nmin): 2
11
10
Notes: Let us look at the sliding window approach through a small illustrative example.
Here, we have a road network and shown in grey, and the black circles are the individual crash locations.

## Slide 62
0
0.2
0.4
0.6
0.8
1.0
Postmile
Fixed window length (w): 0.1 miles
Minimum number of crashes (nmin): 2
0. Dividing the road into equal intervals
1
2
3
5
4
6
7
9
8
1
2
3
5
4
7
9
8
Number of HCCLs identified: 5
Total number of crashes covered: 11
6
6
11
10
11
10
Notes: - Let us assume that the two user inputs in this case are a (fixed) window length of 0.2 miles, and a threshold of 2 crashes
The crash window is placed by using the first crash as a start point. The resulting road segment covered by the crash window forms the first candidate HCCL location.
We now check the total number of crashes within this road segment, which is 2, which is equal to the crash threshold. Hence this qualifies as a HCCL!
We now move on to the second candidate location, which starts from the next available crash as a start point. Here we have three crashes – so it is a HCCL as well!
The next available crash window only contains one crash – so it is not a HCCL
Finally, the last available crash window contains three crashes – so it is a HCCL
In conclusion, we see that the sliding window approach identified 3 HCCLs which covered 8 crashes between them.

## Slide 63
0
0.2
0.4
0.6
0.8
1.0
Postmile
Fixed window length (w): 0.1 miles
Minimum number of crashes (nmin): 2
1. Sliding Window
1
2
3
5
4
6
7
9
8
1
2
3
5
4
6
7
9
8
First candidate HCCL location
(using the first crash as a start point)
Move to the next candidate HCCL location
(use the next available crash as a start point)
Number of HCCLs identified: 4
Total number of crashes covered: 10
# crashes > ncric
11
10
11
10
Notes: - Let us assume that the two user inputs in this case are a (fixed) window length of 0.2 miles, and a threshold of 2 crashes
The crash window is placed by using the first crash as a start point. The resulting road segment covered by the crash window forms the first candidate HCCL location.
We now check the total number of crashes within this road segment, which is 2, which is equal to the crash threshold. Hence this qualifies as a HCCL!
We now move on to the second candidate location, which starts from the next available crash as a start point. Here we have three crashes – so it is a HCCL as well!
The next available crash window only contains one crash – so it is not a HCCL
Finally, the last available crash window contains three crashes – so it is a HCCL
In conclusion, we see that the sliding window approach identified 3 HCCLs which covered 8 crashes between them.

## Slide 64: 1. Sliding Window
Strength:
  Intuitive approach
Weaknesses:
  Fixed HCCL length assumption leads to inefficient HCCL definitions for pedestrians
  Can we improve upon this definition?
7
9
8
Excessive empty space
7
9
8
Notes: - The strength of the sliding window approach is that it is an easy, intuitive approach to follow.
However its weakness is that the fixed HCCL length assumption leads to inefficient HCCL definition, as seen below. Here all the three crashes were located at one point location, but the HCCL was still defined over 0.2 miles.
We also believe that pedestrian-vehicle interactions are more localized, i.e., they occur at intersections, mid-blocks and other crosswalks. So it would be more useful to have compact, dense definitions of HCCLs.
So the question is if we can improve upon this definition?

## Slide 65: Another weakness of sliding window
1
4
7
6
5
3
2
Recommended by Sliding Window
1
4
7
6
5
3
2
Optimal
Fixed window length (w): 0.1 miles
Minimum number of crashes (nmin): 3
The first HCCL identified may not always be the best!

## Slide 66: 2. Dynamic Programming
Dynamic programming (DP) provides a framework to systematically evaluate all possible combinations of HCCLs
Modification to the HCCL definition:
  Relax the fixed window length assumption
  Interpret the user input as the maximum possible crash window size
Notes: -In order to address this question, we employ a new technique called dynamic programming, which provides a framework to systematically evaluate all possible combinations of HCCL definitions.
-In order to use this technique, we made a modification to the HCCL definition, which we thought was reasonable. We relaxed the fixed window length assumption for the HCCLs, and instead interpretted the user input as the maximum possible crash window size. In other words, HCCLs can be smaller in size than the prescribed input, but not bigger than it.

## Slide 67: 2. Dynamic Programming
Has an overarching objective function:
To maximize the overall collision coverage of HCCLs
Notes: -In order to address this question, we employ a new technique called dynamic programming, which provides a framework to systematically evaluate all possible combinations of HCCL definitions.
-In order to use this technique, we made a modification to the HCCL definition, which we thought was reasonable. We relaxed the fixed window length assumption for the HCCLs, and instead interpretted the user input as the maximum possible crash window size. In other words, HCCLs can be smaller in size than the prescribed input, but not bigger than it.

## Slide 68
0
0.2
0.4
0.6
0.8
1.0
1
2
3
4
5
6
7
9
8
Postmile
Number of HCCLs identified: 5
Total number of crashes covered: 11
Maximum window length (w): 0.1 miles
Minimum number of crashes (nmin): 2
2. Dynamic Programming
11
10
Notes: - Now, when we employ the dynamic programming approach, we generate 4 HCCLs of variable sizes. All of them containing as many or more crashes than the prescribed user threshold, and even crash 6 is now covered.

## Slide 69: Average number of crashes per HCCL remains a problem for a DP
Solution: Favoring longer HCCLs wherever possible*
7
9
8
11
10
7
9
8
11
10
*as long as identifying a longer HCCL doesn’t reduce the overall crash coverage of the HCCLs

## Slide 70
0
0.2
0.4
0.6
0.8
1.0
1
2
3
4
5
6
7
9
8
Postmile
Number of HCCLs identified: 4
Total number of crashes covered: 11
Maximum window length (w): 0.1 miles
Minimum number of crashes (nmin): 2
2. Dynamic Programming
11
10
Notes: - Now, when we employ the dynamic programming approach, we generate 4 HCCLs of variable sizes. All of them containing as many or more crashes than the prescribed user threshold, and even crash 6 is now covered.

## Slide 71: 2. Dynamic Programming
Strengths:
  Provides the densest possible HCCL definitions
    All HCCLs start and end with a crash
  Maximizes the total numbers of crashes covered by the HCCLs
Weaknesses:
  DP algorithm may not be as intuitive as the sliding window method
Notes: So the strength of the dynamic programming approach is that it provides the densest possible HCCL definitions. Now there is no empty space at the end of the HCCL, with all HCCLs beginning and ending with a crash.
Also, the this approach maximizes the total number of crashes covered by the HCCLs.
A weakness of the approach its search algorithm may not be as intuitive as the sliding window approach. But that doesn’t implied that it can’t be explained, which we have tried to do in our report in great detail.

## Slide 72
Comparing Sliding Window with Dynamic Programming
Evaluating over 5 years of crash data (2008-2012)

## Slide 73: DP covers more crashes than Sliding Window…
Minimum number of crashes per HCCL, nmin | Maximum HCCL window length, w=0.1 miles |  |  | 
 | Sliding Window |  | DP | 
 | #crashes | #HCCLs | #crashes | #HCCLs
2 | 2985 | 1126 | 3020 | 1161
3 | 1617 | 433 | 1632 | 442
4 | 846 | 173 | 862 | 178
5 | 484 | 80 | 495 | 82
6 | 290 | 41 | 304 | 43
7 | 199 | 25 | 204 | 26
8 | 122 | 14 | 127 | 15
9 | 66 | 7 | 69 | 7

## Slide 74: …and is similar hotspot crash density
Threshold number of crashes per HCCL, nmin | Maximum HCCL window length, w=0.1 miles |  |  |  |  | 
 | Sliding Window |  |  | DP |  | 
 | Average number of crashes per HCCL | Average HCCL length (in miles) | Total miles covered by HCCLs | Average number of crashes per HCCL | Average HCCL length (in miles) | Total miles covered by HCCLs
2 | 2.651 | 0.100 | 112.600 | 2.601 | 0.043 | 49.915
3 | 3.734 | 0.100 | 43.300 | 3.692 | 0.055 | 24.264
4 | 4.890 | 0.100 | 17.300 | 4.843 | 0.063 | 11.237
5 | 6.050 | 0.100 | 8.000 | 6.037 | 0.068 | 5.613
6 | 7.073 | 0.100 | 4.100 | 7.070 | 0.077 | 3.291
7 | 7.960 | 0.100 | 2.500 | 7.846 | 0.085 | 2.218
8 | 8.714 | 0.100 | 1.400 | 8.467 | 0.087 | 1.298
9 | 9.429 | 0.100 | 0.700 | 9.857 | 0.083 | 0.578

## Slide 75: DP requires a smaller area to investigate
Threshold number of crashes per HCCL, nmin | Maximum HCCL window length, w=0.1 miles |  |  |  |  | 
 | Sliding Window |  |  | DP |  | 
 | Average number of crashes per HCCL | Average HCCL length (in miles) | Total miles covered by HCCLs | Average number of crashes per HCCL | Average HCCL length (in miles) | Total miles covered by HCCLs
2 | 2.651 | 0.100 | 112.600 | 2.601 | 0.043 | 49.915
3 | 3.734 | 0.100 | 43.300 | 3.692 | 0.055 | 24.264
4 | 4.890 | 0.100 | 17.300 | 4.843 | 0.063 | 11.237
5 | 6.050 | 0.100 | 8.000 | 6.037 | 0.068 | 5.613
6 | 7.073 | 0.100 | 4.100 | 7.070 | 0.077 | 3.291
7 | 7.960 | 0.100 | 2.500 | 7.846 | 0.085 | 2.218
8 | 8.714 | 0.100 | 1.400 | 8.467 | 0.087 | 1.298
9 | 9.429 | 0.100 | 0.700 | 9.857 | 0.083 | 0.578

## Slide 76: Hazard Assessment
Spot Approach
Hotspots or High Collision Concentration Locations (HCCL) are road segments with a higher than expected number of crashes, compared to prior experience or a user-defined threshold.
Systemic Approach
Systemic approach identifies a set of locations where countermeasures may be installed systemically where roadway facilities share the same unsafe features that are associated with particular crash types.

## Slide 77: The Systemic Approach
FHWA’s Systemic Approach Program.

## Slide 78: The Systemic Approach
FHWA’s Systemic Approach Program.

## Slide 79: Modified Systemic Approach
Crash type is based on features of the crash
e.g., Turning vehicle
Location type is based on features of the site
e.g., Intersection; ADT<10,000; Speed<= 45 mph;Traffic Signal Not present

## Slide 80: CA Systemic Matrix

## Slide 81: CA Systemic Matrix
“Systemic hotspots”

## Slide 82: CA Systemic Matrix
Number of sites

## Slide 83: Countermeasure Selection

## Slide 84: The Systemic Process

## Slide 85: Two sides to the problem

## Slide 86: The Systemic Process

## Slide 87: Improvements across E’s

## Slide 88: Example: Highway crash matrices

## Slide 89: Principles of Road Safety Management
 | 1 | 2
3 | 4 | 5
6 | 7 | 8
A set of goals and activities to improve P/B safety | Infrastructure data | Volume data
Data Evaluation | Hazard Assessment | Countermeasure Selection
Economic Appraisal | Funding Sources | Institutionalization

## Slide 90: Summary
Why Pedestrians and Bicyclists?
Principles of Road Safety Management
Hazard Assessment Strategies
  Hotspot
  Systemic
Successful Road Safety Management System

## Slide 91: Questions

## Slide 92: Road Safety Management System
systemic hotspot
HAZARD ASSESSMENT
Countermeasures
Economic Appraisal
funding
institutionalization
CRASH data
Volume and infrastructure data
Program core
Inputs
Outputs
Evaluation
Support
Legend